## Slide 1: PCB Fabrication in BME

## Slide 2: Board Blanks
Double sided 6 inch x 6 inch
Single sided 6 inch x 6 inch
Single sided 4 inch x 6 inch
All boards 1/16 inch thick
FR4 substrate – glass epoxy
We can shear boards to size, as long as they’re roughly square, BEFORE parts are mounted.

## Slide 3: Drill Sizes
#60 (0.040 inch)
#66 (0.033)
#71 (0.026)
1/8 inch for fasteners
All drills Tungsten Carbide – very hard, very brittle, very fragile

## Slide 4: Board Features
Ideally: 20 mil (0.020 inch) traces 20 mil spacing
We can get away with 10 mil for a few limited cases on a good day.
Put connectors on the perimeter of the board.
It’s OK to have to have a few “air wires” on a single sided board where necessary.
Always place your mounting holes FIRST, then put components around those.

## Slide 5: Other Design Criteria
Double sided boards’ vias are not plated through. To connect from top side to bottom side, you’ll need to solder a wire top and bottom.
Using a component pin as a via to connect top and bottom is OK, most of the time.
Be aware of your limited ability to solder to the component side of certain through-hole components. For example, a chip with a lot of pins will hide a lot of the board beneath it, limiting your ability to solder the component side. Some sockets completely obscure the pads, making it impossible to solder on the component side.

## Slide 6: The PCB etch process
We start with 1:1 PDFs, not Gerbers.
It’s potentially MESSY! Wear old clothes. Clean up after yourselves.
It uses caustic chemicals! You will be provided with gloves and goggles. You must wear closed-toe shoes.
It takes two hours if all goes well. (Actually, it takes Matt about a half hour if he has no “helpers.”)
You must have a steady hand to drill the board. Consider assigning the least-caffeinated member of your team to this task.

## Slide 7: Specifics
A more complete guide to our photolithographic process: https://sites.duke.edu/breezycircuits/category/pcb-etching/
How to generate 1:1 PDFs from Altium Designer: https://sites.duke.edu/breezycircuits/etching-a-board-from-altium-designer/

## Slide 8: Commercial PCB construction
Commercial board houses can do tighter spacing and smaller traces than we can. Expect ~7 mil minimums. Commercial boards will have holes plated through, and will have solder mask and silk screen (text). Odd sizes, outlines, and cut-outs are possible.
PCB Minions is used by several folks around here. (I haven’t yet, but don’t let that stop you.)
https://pcbminions.com/
$50 for 4x6 board in 4 days. $160 for 1 day. You get 5 copies of your board for those prices.